## Slide 1: Towards Dynamic Green-Sizing for Database Servers
Mustafa Korkmaz, Alexey Karyakin, Martin Karsten, Kenneth Salem
University of Waterloo

## Slide 2: Data Center Power Consumption
Chart: Total Power Consumption(tWh)
| 2000 | 2005 | 2013 | 2020
tWh | 28 | 56 | 91 | 140
US in 2013
  12 million Servers
  %2 of all electricity
  Keeps Increasing
Notes: The problem is Data centers consume a lot of power.
According a study in 2013 from Natural Resources Defense Council, there were 12 million servers were in US that operated in data centers in 2013.
(CLICK)These servers consumed around 91 tera watt hour energy. This energy was 2% of all US energy consumption.
(CLICK)And according to projections, power consumption will be increased to 140 tera watts hour in 2020. Which means around 50% increase.
////////////////////////////////////////////////
1) Motivation - data centre power consumption - show how much power data centres consume include an actual stat and graphic to make this point ////////////////////////////////////////////////
Power consumption of data centers has been an important problem for the last decade as the number of servers is increasing rapidly.
In 2013, just in US, there were more than 12 million servers and corresponding electricity consumption was 2% of overall US electricity consumption.
Recent studies also show that the trend in power consumption will continue and 2020 projection shows a 50% increase

## Slide 3: Inside a Data Center
Chart: Power Consumption in Data Centers
| Servers | Cooling | Power Delivery | Other
 | 48 | 28 | 13 | 11
Direct Consumption By The Server Is The Largest Component
Servers Must Also Be Cooled
Chart: Power Consumption in Data Centers
Energy Logic: Reducing Data Center Energy Consumption by Creating Savings that Cascade Across Systems, Emerson Network Power, 2010
Notes: To understand this substantial amount od power consumption, we looked at the components of data centers. Servers’ direct electricity usage is the largest component.
In addition, the cooling devices consume a big portion of energy, where their purpose is to dissipate the server heat.
Overall, servers are the main electricity consumers, directly or indirectly.

## Slide 4: Our Goal
Chart: Power Consumption in Data Centers
| CPU | RAM | HDD | Other
 | 46 | 20 | 6 | 24
Improve Power Efficiency in DBMS
  In-Memory Transactional Workload
Two Parts:
  CPU Power Efficiency
  Memory Power Efficiency
Chart: Power Consumption in a Server
Analyzing the Energy Efficiency of a Database Server, Tsirogiannis et. al., SIGMOD ‘10
Notes: In this work, our contribution is to build a more power efficient servers. We focused on two server hardware.
(CLICK)The first one is DBMS-managed dynamic frequency scaling where we scale CPU power according to the varying workload.
(CLICK) And the second one is DBMS managed memory Provisioning, where we balance memory capacity and power consumption tradeoff

## Slide 5: Improving CPU Power Efficiency
DBMS-Managed Dynamic Voltage & Frequency Scaling
  Slow the CPU at low load to save energy
  Speed the CPU at high load to maintain performance

## Slide 6: Improving Memory Power Efficiency
Details are in the Paper
Reduce Memory Power Consumption by Allowing Unneeded Memory to Idle
  Example: 8 GB DB in 64 GB Server  Up to 56 GB Memory can idle
Not Trivial
  Must control Virtual  Physical  DIMM mapping to use as few DIMM’s as possible
Estimation
  8 GB DB on 64GB Server%40 power reduction over default configuration

## Slide 7: Talk Outline
Motivation & Introduction
DBMS-Managed Dynamic Voltage Frequency Scaling
  Background
  Proposed Work
  Results
Conclusion & Future Work

## Slide 8: Why Power Management in DBMS?
Power is Already Managed
  Hardware & Kernel level
DBMS Has Unique Information
  Workload characteristics
  Quality of Service(QoS): Latency budget
  Database characteristics
    Size, locality

## Slide 9: Database Workload
Workload is not Steady
  Patterns
  Fluctuations, bursts
Systems are Over-provisioned
  Configured for the peak load
Lower Loads?
  Scale power
http://ita.ee.lbl.gov/html/contrib/WorldCup.html

## Slide 10: Dynamic Voltage Frequency Scaling (DVFS)
Recent CPUs Support Multiple Frequency Levels
Can Be Adjusted Dynamically
AMD FX 6300 |  | 
P-State | Voltage | Frequency
P0 | 1.4 V | 3.5 GHz
P1 | 1.225 V | 3.0 GHz
P2 | 1.125 V | 2.5 GHz
P3 | 1.025 V | 2.0 GHz
P4 | 0.9 V | 1.4 GHz

## Slide 11: Existing DVFS Managements
Linux Kernel Supports DVFS Governors
Static, Dynamic Governors
Dynamic Governors
  Sample CPU utilization
  Difference between samples for decision

## Slide 12: DBMS-Managed DVFS
Varying Load
Transaction Latency
Our Approach:
Exploit Latency Budget Except at Peak Load
  Slow down the execution
  Stay under latency budget

## Slide 13: How Slowing Helps
Chart: Energy for Low/High frequencies
| Trx 1 Start | 0 | 60 | 120 | 180 | 240 | 300 | 360 | 420 | 480 | 540 | 600 | 660 | 720 | 780 | 840 | 900 | 960 | 1020 | 1080 | 1140 | 1200 | 1260 | 1320 | 1380 | 1440 | 1500 | 1560 | 1620 | 1680 | 1740 | 1800 | 1860 | 1920 | 1980 | 2040 | 2100 | 2160 | 2220 | 2280 | 2340 | 2400 | 2460 | 2520 | 2580 | 2640 | 2700 | 2760 | 2820 | 2880 | 2940 | 3000 | 3060 | 3120 | Trx 2 Start
Energy(High Freq.) | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Energy(Low Freq.) | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
High Pow | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140 | 140
Low Pow | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Idle Power | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Energy: 0.04 joule
Energy 0.07 joule
Low Frequency is More Power Efficient
High: 0.07 joule
Low: 0.04 joule

## Slide 14: How to Scale Power in DB
Set Frequency Before a Transaction Executes
Predict Response Time for Each Waiting Transaction
Select CPU Frequency Level
  Stay under latency budget
  Slowest possible
Emergency
  High number of waiting transaction
  Set maximum frequency

## Slide 15: DVFS in Shore-MT
Each Worker thread
  Has a transaction wait queue
  Is pinned to a core
  Controls core frequency level
Core 3
Core 2
Core 1
Core 4
Core 5
Core 6
Worker 1
Worker 2
Worker 3
Worker 4
Worker 5
Worker 6

## Slide 16: Latency Aware P-State Selection - LAPS
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150
Latency Budget
600
Trx1 For P4: 150+ 270 = 420
Next P-State
P4
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Wait Time
Service Time Prediction

## Slide 17: Latency Aware P-State Selection - LAPS
P4 is fast enough for Trx1, Check next transaction
Latency Budget
600
Next P-State
P4
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 18: Latency Aware P-State Selection - LAPS
Trx2 using P4 = 670
Latency Budget
600
Next P-State
P4
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 19: Latency Aware P-State Selection - LAPS
P4 is not Fast Enough! Try next Frequency Level
Latency Budget
600
Next P-State
P4
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 20: Latency Aware P-State Selection - LAPS
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150
Trx2 using P3 = 530
Latency Budget
600
Next P-State
P4
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270

## Slide 21: Latency Aware P-State Selection - LAPS
P3 is fast enough for Trx2, set next P-State, Check next transaction
Latency Budget
600
Next P-State
P3
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 22: Latency Aware P-State Selection - LAPS
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx3 using P3 = 660
Latency Budget
600
Next P-State
P3
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 23: Latency Aware P-State Selection - LAPS
P3 is not Fast Enough! Try next Frequency Level
Latency Budget
600
Next P-State
P3
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 24: Latency Aware P-State Selection - LAPS
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx3 using P2 = 510
Latency Budget
600
Next P-State
P3
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 25: Latency Aware P-State Selection - LAPS
P2 is fast enough for Trx3, set next P-State
Latency Budget
600
Next P-State
P2
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 26: Latency Aware P-State Selection - LAPS
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150
All Trxs visited, change state to P2
Latency Budget
600
Next P-State
P2
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270

## Slide 27: Latency Aware P-State Selection - LAPS
Execute Trx1 under P2
Service Time Prediction | 
P-State | Time
P0 | 100
P1 | 120
P2 | 150
P3 | 200
P4 | 270
Latency Budget
600
Next P-State
P2
Trx 3
Wait: 60
Trx 2
Wait: 130
Trx 1
Wait: 150

## Slide 28: Experimental Setup
System:
  AMD FX-6300, 6 cores, 5 P-states , Ubuntu 14.04, Kernel 3.13
  Watts up? Power meter
TPC-C
  12 Warehouses, Single transaction type: NEW_ORDER
Shore-MT
  12 Clients, each issues requests for a different warehouse
  6 Workers, a worker per core, 12 GB buffer pool
Experiment Workloads
  High, Medium, Low offered load

## Slide 29: Results – Medium Load
Medium Load
23 W
42W

## Slide 30: Results – Frequency Residency

## Slide 31: Results – Low Load
Low Load

## Slide 32: Results – High Load
High Load

## Slide 33: Conclusion
DBMS-Managed DVFS
  Exploited workload characteristics
  Transaction Latency Budget
  Reduce CPU power, ensure performance

## Slide 34: Future Work
DBMS Managed CPU Power
  Better Prediction
  Scheduling
DBMS Managed Memory Power
  Workload related capacity/performance decision
  CPU/Memory Hybrid approach

## Slide 35: Thank You
Questions?

## Slide 36: Results

## Slide 37: Results -

## Slide 38: How slowing helps
Chart: Energy consumption
| 1400 | 2000 | 2500 | 3000 | 3500
Joule/Transaction | 0.046476 | 0.049404 | 0.053183 | 0.056789 | 0.070938

## Slide 39: Power Model
Operation Power
  Memory access operations
    ACTIVATE, READ, WRITE
    Optimization is in CPU domain (Cache awareness, algorithm design)
Background Power
  STANDBY(ACTIVE), POWER-DOWN, SELF-REFRESH

## Slide 40: Memory Control Challenges
Default Memory Access: Interleaved
  Use all ranks, data is spread
  Concurrent, multi-rank read/write
Memory Address
  Mapping physical memory ranks to the application

## Slide 41: Proposed Work
Our approach
  Opportunity in scaling background power
  Keep memory ranks in their lowest power state
Non-interleaved
  Store data in the selected ranks
  Activate ranks with increasing memory
  Possible performance degradation

## Slide 42: Results – DRAM Power

## Slide 43: DVFS in Shore-MT
Each worker
  Has a transaction wait queue
  Is pinned to a core
  Controls core frequency level
Clients
  Submit requests to workers
  All pinned to a core

## Slide 44: Improving CPU Power Efficiency
DBMS-Managed Dynamic Voltage & Frequency Scaling
  Slow the CPU at low load to save energy
  Speed the CPU at high load to maintain performance